Adaptive filtering
Used when you have a signal with noise highly correlated with another signal. Can help to reconstruct signals, even when the noise is at the useful frequency and higher amplitude.

---
Papers to cite
1. https://ieeexplore.ieee.org/document/370617

---
How it works
- FIR Filter – Finite Impulse Response
- NLMS – normalized least mean squares method

---
Concept (paraphrased from ref 1)
- We have PPG sensor p, which receives heartbeat signal s, and noise from motion artifacts n0. (p=s+n0)
- We have an accelerometer sensor, which receives noise n1, correlated with n0 (in an unknown way).
- We use a filter to filter n1 to an output y, which we want to be as close as possible to n0.
- We estimate s with s = p – y.

---
To